## Slide 1: DTV Receiver – Hardware Architecture

## Slide 2: Topics
What is DTV?
Benefits of DTV
What is DTV Receiver?
Types of DTV Receiver
Hardware architecture of DTV Receiver
    Tuner
    Demodulator
    CA
    De-Multiplexer
    MPEG Decoder
    NVRAM and Flash
    CPU

## Slide 3: What is DTV
Digital Television (DTV) is a system for transmitting, receiving and viewing higher quality television images and stereo audio.
DTV is completely digital and involves
  Digital cameras
  Digital transmission
  Digital display
The video and audio information is digitized and compressed using the MPEG compression standard (source coding)
DTV Standards
  Digital Video Broadcasting (DVB)
  Advanced Television Systems Committee (ATSC)
  Integrated Services Digital Broadcasting (ISDB)

## Slide 4: Benefits of DTV
  Increased channel capacity such that more channels can be offered within a fixed amount of broadcast bandwidth.
  Increased programming options including interactivity and Video on Demand (VoD).
  Improved picture quality even with a standard-definition signal.
  Improved security to prevent unauthorized persons from receiving services
  Ease of storing data for future use and reprocessing
  Ability to supply more services like
    MHP (Multimedia Home Platform)
    EPG (Electronic Program Guide)

## Slide 5: What is DTV receiver?
DTV stands for Digital TeleVision - Transmitting TV using digital signals
DTV receiver is a set top box that permits the reception of Digital Television. It is usually connected to the TV set or incorporated in the TV set
Functions
  Receives digital TV broadcasts from a cable, satellite or terrestrial network
  Decodes the incoming signal
  Displays good quality pictures
  Outputs digital surround sound
  Renders internet services
  Provides interactive games

## Slide 6: Surround Sound
An audio recording and playback system that uses five or more audio channels plus a subwoofer channel

## Slide 7: Types of Digital TV Receiver
Set-top box (STB)
  Separate box to be connected for receiving Digital data and is connected to a analog TV
Integrated Digital TV (IDTV)
  Receiver is built into a TV set
  Can receive digital or analog broadcasts with no extra hardware
PC with digital tuner card
  Similar to analog TV tuners, except it decodes digital TV signals

## Slide 8: Set Top Box

## Slide 9: SP/DIF
SP/DIF stands for Sony/Philips Digital InterFace
It is a serial interface for transferring digital audio from CD and DVD players to amplifiers and TVs.
It is typically used to transmit PCM and Dolby Digital 5.1, but is not tied to any sampling rate or audio standard.
S/PDIF uses unbalanced 75 ohm coaxial cable up to 10 meters with RCA connectors or optical fiber terminated with a Toslink (Toshiba link) connector.
AES/EBU is the professional version of S/PDIF and uses a higher signal voltage.
They both support the same audio data with slight differences in the frame bits.
Conversion between these interfaces must be handled with electronic circuits, not by adapting one connector to another.

## Slide 10: Hardware Architecture of DTV
10
Return
Path
Tel./Cable/ADSL Modem
Ports:
RS-232; USB
HardDisk
Digital TS
On (Analog)
Carrier Wave
Tuner
De-
mod
Front End
Audio;
Video
MPEG Chip
Memory
MPEG
Decoder
Audio/Video
PES
De-
mux
CA
Module
Back End
Digital TS
PSI/SI;CA; iTV Data
Graphics & OSD Generator
CPU
Memory
CPU
Data
Packets
(Sections)
Subtitles

## Slide 11: Tuner
Tuner is a device which receives RF analog signal and outputs the MPEG Transport Stream
Tuners can be divided into three broad categories:
Broadcast In-band (IB) Tuner: Once the signal arrives from the physical transmission media, the IB tuner will isolate a physical from a multiplex of channels and convert to baseband. The term ‘’baseband’’ is used to describe a single channel or digital signal, extracted from broadband signal which is basically a stream of multiple channels.
Out Of Band (OOB) Tuner: This type of tuner facilitates the transfer of data between the head-end systems and the set-top box. They are widely used in cable set-top boxes for providing subscribers with medley of interactive services. Implementations of the OOB tuner tend to operate within 100 to 350 MHz frequency band.
Return Path Tuner: This tuner allows a subscriber to activate the return of path and send data back to the interactive services provider. Implementations of this tuner tend to operate within the 5 to 60 MHz frequency band.

## Slide 12: Demodulator
Transmission mechanism | Modulation
Satellite | QPSK
Cable | QAM
Terrestrial | OFDM
Modulation schemes in DTV network
Demodulator converts the Analog signal to Digital signal
Then, it checks for errors and forward the bit stream to the demultiplexer

## Slide 13: Conditional Access
Conditional Access (CA) is the protection of content by requiring certain criteria to be met before granting access to this content
Access to the content is provided only to those with valid decryption smart cards
Algorithm is proprietary to the user
  e.g. DVB Common Scrambling Algorithm
Scrambling and Encryption are used
Scrambling Vs Encryption
  Scrambling is a technique used to distort or garble (a signal) so as to render it unintelligible without a special receiver
  Scrambling is a form of analogue signal manipulation that is applied pseudo-randomly to analogue signals, generally under the control of an encrypted digital code that is transmitted in the vertical interval of the television signal.
  Encryption is a process of combining the entire digital bit stream representing the digital television signal with a digital encryption code.

## Slide 14: De-Multiplexer
Demultiplexer takes an MPEG-2 transport stream and locates the required elements
    Audio and video streams
    Broadcast data streams
    Service information
    Some service information for the network are also added
Demultiplexer passes these streams on to other parts of the system
  Service information and data streams to the CPU (if it is interested)
  Audio and video to the MPEG decoder
Other data from the transport stream is thrown away
Demultiplexer may include section filtering capability to filter other MPEG-2 sections as requested by applications

## Slide 15: MPEG Decoder
MPEG Decoder decodes audio and video MPEG streams and displays them on the screen
It may include support for graphical overlays
  Cursor, graphics
  Some receivers support up to five graphics planes
    Background, video, two graphics planes, cursor
It may include support for scaling, clipping and repositioning video, but this may be limited
It is typically combined with the graphics processor
  Makes it easier to integrate different elements of the display

## Slide 16: NVRAM and Flash
NVRAM (Non Volatile RAM) stores the configuration information, which may include:
  Country Code
  Language Preferences - OSD, Audio, Subtitle
  Audio Mode – Mono, Stereo, Left, Right
  Volume Level
  OSD Transparency
  Last Viewed Channel – Channel No, Service ID, Service Type
  Channel Lock Password
  Display Parameters – Brightness, Contrast, Saturation, Tint
  Software Version
Flash stores the following details:
  Applications and system software
  Frequency Database
  Service Database
  Country Database
  Icons used in the platforms

## Slide 17: CPU
CPU handles all of the other tasks in the system
  Decoding and handling service information
  Decoding broadcast data streams
  User interaction
  Running built-in or downloaded applications
It is integrated with the MPEG-2 decoder and other components in most of the cases

## Slide 18
Thank you