## Slide 1: DTV Receiver – Software Architecture

## Slide 2: Topics
Software Architecture of DTV Receiver
    Middleware
    SI Parser
    Database
    Teletext
    Subtitle
    EPG
    UI Framework

## Slide 3: Software Architecture of DTV

## Slide 4: Middleware
DTV Middleware provides a common software platform for application development
It is usually a C or Java code
Every middleware platform has basically the same features
  e,g. Graphics & video manipulation, return channel access, access to service information, etc.
Various modules of DTV Middleware are:
  SI Parser
  Service Database
  Tele text
  Subtitles
  EPG
  Parental Control
  UI Framework

## Slide 5: SI Parser
SI (Service Information) Parser
  SI is responsible for collecting MPEG,DVB tables and Parsing
  SI is also responsible for parsing all the descriptors
  Updates database with service and events information
  Monitor the version change
  Generally SI parser module is divided as
  SI Capture
  SI Parser
Service Database
  Used for storing service and tuning information
  Interfaces to be provided to application such as add, delete, move, sort, store, reload etc
  Common database interface API’s for accessing service data from the different database

## Slide 6: Database
Used for storing service and tuning information
Interfaces to be provided to application such as add, delete, move, sort, store, reload etc
Common database interface API’s for accessing service data from the different databases
Pan-European requirements
    Service Replacement
    Logical Channel Number
    Parental Control
    Duplicate Service

## Slide 7: Teletext
Teletext provides public information such as
    Local Weather
    Sports News
    Train Timings
    Stock Exchange etc
Teletext is organized as magazines and pages
Users can navigate through either through embedded links of by page numbers directly.
Teletext Service is carried in a separate PID and is broadcast periodically
Typically these pages are cached in memory for faster access

## Slide 8: Subtitle
Subtitle is a visual representation of speech (audio)
    For Languages other than transmitted audio
    For hearing impaired persons
Subtitles are transmitted as
    Text
    Graphics
Subtitles are of 2 types
    Open - Part of video
    Closed – Can be hidden
Subtitles comes as PES packets in a separate PID

## Slide 9: Subtitle (contd)
They need to extracted, decoded and overlaid on video.
    Graphics Subtitles are RLE (Run Length Encoding) encoded
    Indexed Formats are used
    Overlays can timeout
Subtitles are synched with the video based on their presentation time stamps
Subtitles are organized hierarchically
    Page – Entire Canvas
    Regions - Rectangular
    Objects

## Slide 10: Electronic Program Guide
EPG is a electronic equivalent of TV events page in newspaper
EPG provide detail information about the event schedule such as start time, duration, rating etc.
Events are classified in different categories such as Sports, Movies, News, etc
EPG also provides short and long description about the event
EIT Present/Following table will carry current/next event information
EIT0-15 tables will carry schedule event information
EPG database for maintaining all the event information

## Slide 11: UI Framework
GUI Framework will have common logic used by applications
Provide controls such as list, button etc
Provide region management such creation, deletion etc
Provide support for palette, Bitmap display, drawing routine etc.
Provide support for color conversion routines
Provide fonts support
Support for compression for icons and bitmaps

## Slide 12
Thank you